#include <DHT.h>
#include <DHT_U.h> // importing libraries
#define DHTPIN 4 // connect communication wire to pin 4 on esp32 board
#define DHTTYPE DHT22
DHT dht(DHTPIN, DHTTYPE);



void setup() {
  // put your setup code here, to run once:
   Serial.begin(9600);
  //dht start
  dht.begin();

}

void loop() {
  // put your main code here, to run repeatedly:

  
  // Reading temperature or humidity takes about 250 milliseconds!
  float h = dht.readHumidity();
  // Read temperature as Celsius (the default)
  float t = dht.readTemperature();
  // Read temperature as Fahrenheit (isFahrenheit = true)
  float f = dht.readTemperature(true);

  // Check if any reads failed and exit early (to try again).
  if (isnan(h) || isnan(t) || isnan(f)) {
    Serial.println(F("Failed to read from DHT sensor!"));
    return;
  }


  Serial.print(F("Humidity: "));
  Serial.print(h);
  Serial.print(F("%  Temperature: "));
  Serial.print(t);
  Serial.print(F("°C "));
  Serial.print(f);



}